MSP430 in Fedora
Cheap Hardware Hacking
PRESENTED BY:
Martin Bříza
m@rtinbriza.cz

---
Today's Topics
- Examples
- MSP430
- The MSP430 Launchpad
- Tools in Fedora
- Resources

---
Examples

---
Alarm clock
http://dangerousprototypes.com/forum/viewtopic.php?f=56&t=2784&p=53277#p53277

---
Biofuel (Beer) Fermentation Controller
http://www.benhavey.com/projects/biofuel.html

---
Line following robot
http://buildsmartrobots.ning.com/profiles/blogs/hacking-the-hexbug-spider-using-the-no-solder-hacking-kit-from-em

---
RGB LED Coffee Table Spectrum Analyzer
http://e2e.ti.com/group/launchyourdesign/m/msp430microcontrollerprojects/447779.aspx

---
MSP430

---
Texas Instruments
- Inventors of transistor, microchip and calculator
- Portfolio: analog and digital signal processing, calculators, integrated circuits...
- Several types of processors (ARM, OMAP and their own designs)
- You can request samples of their chips for free

---
MSP430
- 16 bit CPU, up to 25 MHz
- Up to 256KB flash and 16KB RAM
- Optional peripherals
  - ADC, DAC, PWM
  - SPI, I2C, DMA, USB
- Programmable via JTAG and RS232
- Low cost, low power consumption

---
Value Line
- 1.8V – 3.6V operation voltage
- Up to 16MHz speed
- 512B – 16KB flash
- 128 – 512B RAM
- Up to 24 GPIO pins
- Two of them are shipped with the Launchpad

---
The Launchpad

---
Properties
- Up to 20 pin DIP socket
- Mini-USB port
- Supports programming and runtime debugging of the chip
- 2 programmable LEDs
- 1 Programmable and 1 reset button
- All pins are broken out on the board
- Price: $9.99

---
Booster Packs
- First, only the Capacitive Touch from TI
- Over time, more manufacturers added their products
- Various displays
- Sound – MIDI, mp3
- Wireless communication
- Sensors – movement, temperature, ...

---
The Tools

---
Example source - foo.c
#include <msp430.h>
int main(void) {
// stop the watchdog
WDTCTL = WDTPW + WDTHOLD;
// set first pin to output and set it to high
P1DIR |= BIT0;
P1OUT |= BIT0;
while(1) {
int i;
// small inaccurate delay
for (i = 0; i < 0xAFFF; i++);
// toggle the output between low and high (LED blinks)
P1OUT ^= BIT0;
}
}

---
msp430-gcc
- Works exactly like your regular GCC
- You have to specify the MCU due to their different features
- Support for work with ports and interrupts
- Example usage:
  msp430-gcc -mmcu=msp430g2231 foo.c -o foo.elf

---
mspdebug
- Tool for flashing and debugging your programs
- Invoke with:
  mspdebug rf2500
- And inside mspdebug, for example:
  prog foo.elf
  run
- Will load the program and start it

---
Resources

---
Friendly Launchpad
- Not an actual resource, rather a library
- Makes you able to compile Arduino or Arduino-like source code
  https://github.com/chrishulbert/friendly_launchpad

---
Texas Instruments Official
- MSP430G2 Value Line
- MSP430 Launchpad
- Launchpad Wiki
- Booster packs
- Aggregated open source projects

---
External Resources
- Hack a Day tag
- 43 oh! - website dedicated to the MCU
- Dangerous Prototypes tag
- MSP430 subreddit
- Instructables tag

---
Questions?
CONTACT:
m@rtinbriza.cz, mbriza@redhat.com
SLIDES AVAILABLE ON:
http://mbriza.fedorapeople.org/msp430.odp